## Slide 1: CCDs And Data Reduction
ASTR 257

## Slide 2
A CCD (Charge-Coupled Device) is a 2D Array of Light-Sensitive Pixels that Reads out in a Particular Way
CCDs are small
Most digital cameras you use are CCDs
In astronomy, they can only measure 1 wavelength at a time
In color digital cameras, pixels that are sensitive to difference colors are interleaved

## Slide 3: CCD Readout

## Slide 4: Photoelectrons
CCDs absorb photons and turn them into electrons
Electrons are turned into numbers with an analog-to-digital converter
The analog-to-digital converter has error each time it reads a pixel. This is called read noise.
The analog-to-digital converter cannot make negative numbers. So a bias is added to each pixel so that the read-out will always register a positive number, even in the face of read noise

## Slide 5: Pixel-by-pixel properties
Bias—positive number added to each pixel. Does not change significantly from frame to frame. Does not change with integration time. Correct with Bias Frame
Dark Current—Electrons that build up with time due to thermal effects in the CCD. Correct with Dark Frame
Gain—Number of photoelectrons produced per photon. Usually known a priori, but can be calculated with Poisson statistics.
Quantum Efficiency—fraction of photons detected. Correct with flat field.

## Slide 6: Types of Data
Bias Frame—Ideally a zero second image that captures the per-pixel bias, but no light and no dark current. Counts are from bias.
Dark Frame—Frame with a non-zero integration time taken with the camera shutter closed. Counts are from bias and dark current.
Flat Field—Frame with non-zero integration time taken of the twilight sky or a special screen on the dome that has uniform brightness. Counts are from bias, dark current and a uniform source.
Science Frame—Counts are from bias, dark current and a science field. Each pixel in a science image is counts=science*QE+dark+bias

## Slide 7: Standard Data Reduction
If all integration times are the same:
Calibrated Image = (science-dark)/(flat-dark)

## Slide 8: Standard Data Reduction
Make Dark Image—Subtract bias frames from dark frames. Divide by integration time to make into a per second image
Make Flat Field Image—Subtract dark frame (or just darker frame). Divide by integration time to make into a per second image.
Make Science Frames—Subtract bias frame. Divide by integration time to make into a per second image. Subtract Dark Image. Divide by Flat Field.
NOTE: Since the flat field has an unknown illumination, pixel values are all scaled by an unknown constant. With few exceptions, astronomy data reduction is done in a relative not absolute sense!!

## Slide 9: Other Issues: Cosmic Rays Make Artifacts on Your CCD
Solution: Take lots of images and median them

## Slide 10: Other Issues: Persistently Bad Pixels
Solution: Take the average of the surrounding pixels or
“dither” the telescope to multiple different positions, then shift the images to overlap and median combine

## Slide 11: Other Issues: Saturation
Solution: Take short enough integrations that the detector is not saturated
…but when you use shorter integrations, you read the detector more times and each time you get read noise.

## Slide 12: Ds9 demo
scale/stretch
color
blinking
lock-physical
regions
centroiding
projection tool
world-coordinate system